Station Ground

A happy station is a properly grounded one! Many people overlook the necessity of a good ground system and their stations will suffer because of that. A good ground system is neither expensive or difficult to install.

The biggest benefit a good ground system is that of SAFETY! Should your transmitter develop a problem, UNGROUNDED, there is the possibility of LETHAL VOLTAGES being present on the chassis of the transmitter! This means that you could be electrocuted from simply touching your rig! NOT COOL! Now the same transmitter with the same problem, GROUNDED, will simply "Blow" the AC power fuse and prevent you from receiving any kind of shock! Much Better! This also brings me to another....

NEVER OPERATE YOUR TRANSMITTER UN-FUSED!

If it keeps blowing the fuse, DO NOT USE A BIGGER FUSE!

THIS IS A GOOD WAY TO GET HURT OR KILLED!

Another benefit to a proper ground system is that your transmitter will "Tune Up" much more easily and quite possibly give you better "On Air" performance as far as coverage goes. A ground for a transmitter will also help to reduce or eliminate any potential QRM problems! This in itself should be enough to motivate you to ground your station.

"OK, I'm convinced! What do I need to do now?" That depends on a couple of things. Your ground will perform best, RF-wise, if you can keep the length of wire connecting your transmitter to the ground rod as short and as large as possible. So with this in mind, try to figure out the best location for planting your ground rod. "Can't I use the traditional Cold Water Pipe connection as a ground?". Unless your house is old, the probability of PVC or PLASTIC pipe being used to service your house is very high. This means that the cold water pipes running throughout your house probably will not be a good ground. The only way to be sure is to plant your own ground rod.

Ground Rods are commonly available through Electrical Supply Houses. Get one that is around EIGHT feet in length, the longer the better. Your better ground rods will be copper coated steel. You can expect to pay in the neighborhood of $15 for a suitable rod. DO NOT USE THE RADIO SHACK 4 FOOT SPECIALS! They are a waste of time because they are not long enough!

Now that you have your ground rod, it's plantin' time! Get a ladder and a sledge hammer and with much manual labor, drive that rod down until only 3 or 4 inches are remaining above ground.

Connecting the ground rod to the transmitter can be done in several ways. There are a couple of important items that should be observed. The first is to keep the length of the connecting wire as short as possible. Second, use as heavy gauge (Bigger) wire as you can. Last, make sure the wire is one, continuous piece. I have used Romex wire for my ground. Romex is the three conductor wire used for AC wiring in most homes. For best results use all three wires these can be easily stripped out for your ground system. The other alternative is to use the ground braid of the larger coax cable like RG-8. If you have old cable that is no longer suitable for feeding an antenna, it will make quite handy ground wire. Again, this can be stripped out but is a little more difficult and time consuming to do.

The connection of the wire to the ground rod can be done with a couple of automotive type hose clamps. Get small ones just big enough to accommodate the wire and rod. Make sure and clean the rod so it's nice and shiney before you make the connection. After you make the connection, paint the exposed rod and connection with Day Glo orange paint to help prevent oxidation and so no one trips over it or runs over it with the lawn mover!

Connecting the wire to the transmitter can be done either by connecting the wire directly to the CHASSIS, and there is usually a screw terminal for this purpose or you can get fancy by using a Lug terminal to make the connection. Either way is fine.

Now that your transmitter is properly grounded, this point at where the ground rod is connected can and should be used as a connection point to ground the rest of your station equipment as needed.

Now for those of you who want the ultimate ground system , here are some more helpful hints. Use multiple ground rods. Two rods will work better than one and four ground rods will perform better that two. Multiple rods will perform best when placed farther apart than they are long. If you use multiple rods, just remember to connect all rods to a single connecting point. Another helpful tip for those who live in areas where soil conductivity is a problem, before you drive your rod, take a post hole digger and dig a post hole down about three feet, drive your rod down the center of this hole and then fill the hole with water softener salt up to about 6 inches from the top of the hole. Fill the rest of the hole with dirt and then the rain will leach out the salt into the soil and increase your ground rod's effectiveness. The downside of this approach is that is salt is corrosive to copper and will destroy your ground rod sooner than normal.

If you ive on the Second or Third story of a apartment building and can't really install a ground? Not a problem, while not as effective as a "True Ground" a "Counterpoise" can be used to help compensate for the lack of a ground rod. A counterpoise is nothing more than a wire that is at least one wavelength long. It is then connected to a transmitters ground terminal and will function somewhat as a ground. To figure out the length of your counterpoise wire, see the section on Antennas. Another alternative is to use a artificial ground. MFJ manufactures one, The Model # is MFJ-931 and lists for $80 and could provide you with alternative ground.

GROUNDING FOR CABLE TV AND SATELLITE SYSTEM ANTENNAS

Dr. Richard L. Cohen

The National Electrical Code requires that coaxial cable sheaths be "properly grounded" where they enter  the building. This grounding is required so that AC power voltages (from an accidental contact with power  lines) or lightning currents (from lightning strikes to or near the dish or cables) are drained off before they  get inside the residence.

Because lightning currents can be so large, the code sets up strict requirements for the grounding.

For example:

1. The grounding must be to the building grounding electrode system (Article 820-40(b)). Correct  grounding points are, for example, the power service entrance ground, the building grounding electrode, or  a permanently grounded metal waterpipe (See the NEC for full details).

2. A driven ground rod is not adequate grounding.(Comment on p. 904 of the 1993 Handbook). If a  driven ground rod is used, it must be bonded to the building grounding electrode system with a #6 copper  wire (Article 820-40(d)).

3. The code is not definite on the conductor size required to connect the sheath of a coaxial cable to the  building ground. Panamax recommends a #8 or larger copper wire for satellite systems cables, and a #12  wire for CATV coax cables.

4. The NEC appears to require bonding satellite dish grounds to the house ground (Article 810-20). The  code requires a conductor of a least #10 copper wire to bond the dish to the house ground (Article  810-21).

Direct-strike lightning currents are extremely large (up to 100,000 Amperes), and violate people's intuition  and experience about electricity. Even the attenuated lightning current (1,000-10,000 Amperes) at the end  of a coaxial cable sheath is much larger than currents one normally deals with. For currents of this size, a  driven ground rod (typically 10 - 100 Ohms) is almost useless, and even the #14 green wire ground in  residential wiring systems develops enormous voltage drops while carrying away the lightning currents.  That's why bonding directly to the building electrode system is so important - it limits the development of  big voltage drops within the building wiring system.

© 1996 Panamax

Grounding is key to good reception

From: jpd@space.mit.edu (John Doty)

Newsgroups: rec.radio.shortwave

Subject: Grounding is key to good reception, was: Experience w/NRD-535

Date: 16 Feb 1995 16:36:40 GMT

In article <825_9502140342@tor250.org> Larry.Picard@odxabbs.tor250.org (Larry Picard) writes:

In your recent post you advised that coax should be grounded at two sites, first at the antenna and then just  before entering the house. Is there an advantage in grounding at more than these sites?

With grounds the most common experience is "the more the merrier". As you add more, however, you usually reach a

diminishing returns (no pun intended) situation where there is no *observable* improvement: that's usually a good place to stop. There are also exceptional circumstances where grounding increases noise problems, but these, in my experience, are much rarer than the pundits who preach against "ground loops" seem to think.

Even a semi-quantitative theoretical treatment of grounding in oversimplified situations requires heavy math at RF. Experimentation is thus required even if one has done elaborate calculations. It's often easier to use the theory as a guide to what to try, and then experiment.

I would also assume that the antenna is grounded when it is connected to the receiver as the outer braid of  the coax is in continuity with the receiver chassis.  What's ground? If connect the shield of my coax (which is grounded outside) to the antenna input of my R8, I hear lots of junk, indicating that there is an RF voltage difference between the coax shield and the R8 chassis. Last night this measured about S5.5, which is about -93 dBm (preamp off, 6KHz bandwidth). That's a lot of noise: it was 18 dB above my antenna's "noise floor", and 26 dB above the receiver's noise floor.

This sort of disagreement about ground potential is characteristic of electrically noisy environments. The receiver will, of course, respond to any voltage input that differs from its chassis ground. The antenna, on the other hand, is in a very different environment, and will have its own idea of what ground potential is. If you want to avoid noise pickup, you need to deliver a signal, referenced at the antenna to whatever its ground potential is, in such a way that when it arrives at the receiver, the reference potential is now the receiver's chassis potential.

Coaxial cable represents one way to do this. Coax has two key properties:

1. The voltage between the inner conductor and the shield depends only on the state of the electromagnetic field within the shield.

2. The shield prevents the external electromagnetic field from influencing the internal electromagnetic field (but watch out at the ends of the cable!).

So, it's easy, right? Run coax from the antenna to the receiver. Ground at the antenna end will be whatever the antenna thinks it is, while ground at the receiver end will be whatever the receiver thinks it is. The antenna will produce the appropriate voltage difference at the input side, and the receiver will see that voltage difference uncontaminated by external fields, according to the properties given above.

Unfortunately, it doesn't quite work that way. It's all true as far as it goes, but it neglects the fact that the coax can also guide noise from your house to your antenna, where it can couple back into the cable and into your receiver. To see how this works, let me first describe how this noise gets around.

The noise I'm talking about here is more properly called "broadband electromagnetic interference" (EMI). It's made by computers, lamp dimmers, televisions, motors and other modern gadgets. I have all these things. In many cases, I can't get them turned off, because it would provoke intrafamilal rebellion. However, even when I turn them off, the noise in the house doesn't go down very much, because my neighbors all have them too. In any case, one of the worst offenders is my computer, which is such a handy radio companion I'm not about to turn *it* off.

Some of this noise is radiated, but the more troublesome component of this is conducted noise that follows utility wires. Any sort of cable supports a "common mode" of electromagnetic energy transport in which all of the conductors in the cable are at the some potential, but that potential differs from the potential of other nearby conductors ("ground"). The noise sources of concern generate common mode waves on power, telephone, and CATV cables which then distribute these waves around your neighborhood. They also generate "differential" mode waves, but simple filters can block these so they aren't normally a problem.

So, let's say you have a longwire antenna attached to a coaxial cable through an MLB ("Magnetic Longwire Balun" [sic]). Suppose your next door neighbor turns on a dimmer switch. The resulting RF interference travels out his power lines, in through yours, through your receiver's power cord to its chassis, and out your coaxial cable to your MLB. Now on coax, a common mode wave is associated with a current on the shield only, while the mode we want the signal to be in, the "differential" mode, has equal but opposite currents flowing on shield and inner conductor. The MLB works by coupling energy from a current flowing between the antenna wire and the coax shield into into the differential mode. But wait a second: the current from the antenna flows on the coax shield just like the common mode current does. Does this mean that the antenna mode is contaminated with the noise from your neighbor's dimmer?

The answer is a resounding (and unpleasant) yes! The way wire receiving antennas work is by first moving energy from free space into a common mode moving along the antenna wire, and then picking some of that off and coupling it into a mode on the feedline. In this case, the common mode current moving along the antenna wire flows into the common mode of the coax, and vice versa. The coax is not just feedline: it's an intimate part of the antenna! Furthermore, as we've seen, it's connected back through your electrical wiring to your neighbor's dimmer switch. You have a circuitous but electrically direct connection to this infernal noise source. No wonder it's such a nuisance!

The solution is to somehow isolate the antenna from the common mode currents on the feedline. One common way to do this is with a balanced "dipole" antenna. Instead of connecting the feedline to the wire at the end, connect it to the middle. Now the antenna current can flow from one side of the antenna to the other, without having to involve the coax shield. Unfortunately, removing the necessity of having the coax be part of the antenna doesn't automatically isolate it: a coax-fed dipole is often only slightly quieter than an end-fed longwire. A "balun", a device which blocks common mode currents from the feedline, is often employed. This can improve the situation considerably. Note that this is not the same device as the miscalled "Magnetic Longwire Balun".

Another way is to ground the coaxial shield, "short circuiting" the common mode. Antenna currents flow into such a ground freely, in principle not interacting with noise currents. The best ground for such a purpose will be a earth ground near the antenna and far from utility lines.

Still another way is to block common mode waves by burying the cable. Soil is a very effective absorber of RF energy at close range.

Unfortunately, none of these methods is generally adequate by itself in the toughest cases. Baluns are not perfectly effective at blocking common mode currents. Even the best balun can be partially defeated if there's any other unsymmetrical coupling between the antenna and feedline. Such coupling can occur if the feedline doesn't come away from the antenna at a right angle. Grounds are not perfect either. Cable burial generally lets some energy leak through. A combination of methods is usually required, both encouraging the common mode currents to take harmless paths (grounding) and blocking them from the harmful paths (baluns and/or burial).

The required isolation to reach the true reception potential of the site can be large. According to the measurements I quoted above, for my site the antenna noise floor is 18 dB below the conducted noise level at 10 MHz. 18 dB of isolation would thus make the levels equal, but we want to do better than that: we want the pickup of common mode EMI to be insignificant, at least 5 dB down from the antenna's floor. In my location the situation gets worse at higher frequencies as the natural noise level drops and therefore I become more sensitive: even 30 dB of isolation isn't enough to completely silence the common mode noise (but 36 dB *is* enough, except at my computer's CPU clock frequency of 25 MHz).

Getting rid of the conducted noise can make a huge difference in the number and kinds of stations you can pick up: the 18 dB difference between the conducted and natural noise levels in the case above corresponds to the power difference between a 300 kW major world broadcaster and a modest 5 kW regional station.

The method I use is to ground the cable shield at two ground stakes and bury the cable in between. The scheme of alternating blocking methods with grounds will generally be the most effective. The ground stake near the house provides a place for the common mode noise current to go, far from the antenna where it cannot couple significantly. The ground stake at the base of my inverted-L antenna provides a place for the antenna current to flow, at a true ground potential relative to the antenna potential. The buried coax between these two points blocks noise currents.

There has been some discussion of grounding problems on this and related echos. I believe it has been  mentioned that electrical codes require that all grounds be tied together with heavy guage wire.

I'm no expert on electrical codes, and codes differ in different countries. However, I believe that any such requirement must refer only to grounds used for safety in an electric power distribution system: I do not believe this applies to RF grounds.

Remember that proper grounding practice for electrical wiring has very little to do with RF grounding. The purpose of an electrical ground is to be at a safe potential (a few volts) relative to non-electrical grounded objects like plumbing. At an operating frequency of 50/60 Hz, it needs to have a low enough impedance (a fraction of an ohm) that in case of a short circuit a fuse or breaker will blow immediately.

At RF such low impedances are essentially impossible: even a few centimeters of thick wire is likely to exhibit an inductive impedance in the ohm range at 10 MHz (depends sensitively on the locations and connections of nearby conductors). Actual ground connections to real soil may exhibit resistive impedances in the tens of ohms. Despite this, a quiet RF ground needs to be within a fraction of a microvolt of the potential of the surrounding soil. This is difficult, and that's why a single ground is often not enough.

A little experimentation with my radio showed that the chassis was directly connected to the third  (grounding) prong of the wall plug. I am concerned that by connecting my receiver to an outside ground I  am creating a ground loop that involves my house wiring. Can you comment on this?

Yes, you have a "ground loop". It's harmless. In case of a nearby lightning strike it may actually save your receiver. My R8 isn't grounded like that, so I had to take steps to prevent the coax ground potential from getting wildly out of kilter with the line potential and arcing through the power supply. I'm using a surge supressor designed to protect video equipment: it has both AC outlets and feedthroughs with varistor or gas tube clamps to keep the various relative voltages in check. Of course the best lightning protection is to disconnect the receiver, but I'm a bit absent minded so I need a backup.

This may seem like a trivial point but I recently discovered that the main ground from the electrical service  panel in my house was attached to a water pipe which had been painted over. I stripped the paint from the  pipe and re-attached the grounding clamp and I noticed a reduction in noise from my receiver.

Not trivial. Not only did you improve reception, but your wiring is safer for having a good ground.

I suspect part of the reason I see so much noise from neighbors' appliances on my electric lines may be that my house's main ground wire is quite long. The electrical service comes in at the south corner of the house (which is where the breaker box is), while the water (to which the ground wire is clamped) enters at the east corner. All perfectly up to code and okay at 60 Hz, but lousy at RF: if it was shorter, presumably more of the noise current would want to go that way, and stay away from my receiver.

I am also a little confused by what constitues an adequate ground. I have read that a conducting stake  driven into the ground will divert lightning and provides for electrical safety but that RF grounding systems  have to be a lot more complex with multiple radials with lengths related to the frequencies of interest. Is this  true?

Depends on what you're doing. If you're trying to get maximum signal transfer with a short loaded (resonant) vertical antenna with a radiation resistance of, say, 10 ohms, 20 ohms of ground resistance is going to be a big deal. If you're transmitting 50 kW, your ground resistance had better be *really* tiny or things are going to smoke, melt or arc.

On the other hand, a ground with a resistance of 20 ohms is going to be fairly effective at grounding a cable with a common mode characteristic impedance of a few hundred ohms (the characteristic impedance printed on the cable is for the differential mode; the common mode characteristic impedance depends somewhat on the distance of the cable from other conductors, but is usually in the range of hundreds of ohms). Of course, if it was lower a single ground might do the whole job (but watch out for mutual inductance coupling separate conductors as they approach your single ground).

In addition, a ground with a resistance of 20 ohms is fine for an unbalanced antenna fed with a high impedance transformer to supress resonance. Such a nonresonant antenna isn't particularly efficient, but high efficiency is not required for good reception at HF and below (not true for VHF and especially microwave frequencies).

Much antenna lore comes from folks with transmitters who, armed with the "reciprocity" principle, assume that reception is the same problem. The reciprocity principle says that an antenna's transmission and reception properties are closely related: it's good physics, but it ignores the fact that the virtues required of a transmitting and receiving antenna are somewhat different. Inefficiency in a transmitting antenna has a direct, proportional effect on the received signal to noise ratio. On the other hand, moderate inefficiency in an HF receiving antenna usually has a negligible effect on the final result. A few picowatts of excess noise on a transmitting antenna has no effect on its function, but is a big deal if you're receiving (of course, one might not want to have transmitter power going out via unintended paths like utility lines: this is indeed the "reciprocal" of the conducted noise problem, and has similar solutions).