Radio Log Book Recommendations

The log book must have the following sections: (Ref AUXCOM Course Chap 7)

Log Section – (Atch 1)

Message Section

- Recommend lined loose leaf paper.

- Include note on conversion for ZULU Time (in our time zone, add 5 hours to local when on EST, add 6 hrs when on DST).

- It is recommended that you keep a tape recorder at your station to record any critical message traffic involving a distress, etc. so you can write record afterwards.

Reference Section

1.  List of VHF Marine Channels and uses (Atch 2)

2. Flotilla Calling Tree /Division/Flotilla Contacts (ERP Annex G1 & G2)

3. List of Division 6 Operational Facilities (OPFACS and RADFACS) from the 	Emergency Response Plan Annex F

4. .List of Sector Coast Guard Telephone Numbers from the Emergency Response 	Plan, Chapter 3 Annex B.

5. List of local Emergency Numbers, to include:

Local City/County Police

State Police

Local/County Fire Department

Emergency Management

Virginia Marine Police (see http://www.mrc.state.va.us/mrc-field-							offices.shtm)

6. Copies of SAR Incident Report  (http://forms.cgaux.org/archive/a7034f.pdf)

7. Local Area Marine Chart Pages (or separate Chart Book or Charts, Road 		Maps)

8. List of Launch and Recovery Sites (ERP Annex E)

9. Sector Hampton Roads AUXOP Supplement (GPHRINST 16790) Comms Sections 16, 17, and 18.

Separately, unless you have emergency/battery power for a computer, the Division Emergency Response Plan and other references recommended on Division Comms Page.

Radio Log

U.S. Coast Guard Auxiliary Radio Facility

| Date | Time Begun | Time Ended | Frequency | Station Called | Message Summary | Operator |
| --- | --- | --- | --- | --- | --- | --- |

U.S. VHF Marine Radio Channels and Frequencies MHz

Channel

Transmit	 Receive   		Use

01A    156.050	156.050	Port Operations and Commercial, VTS.  Available only in New Orleans / Lower Mississippi area.

05A	 156.250	156.250	Port Operations or VTS in the Houston, New Orleans and Seattle areas.

06	156.300	156.300	Intership Safety

07A	 156.350	156.350	Commercial

08	 156.400	156.400	Commercial (Intership only)

09	 156.450	156.450	Boater Calling.  Commercial and Non-Commercial.

10	 156.500	156.500	Commercial

11	 156.550	156.550	Commercial.  VTS in selected areas.

12	 156.600	156.600	Port Operations.  VTS in selected areas.

13	 156.650	156.650	Intership Navigation Safety (Bridge-to-bridge).  Ships	  >20m length maintain a listening watch on this channel in US waters.

14	 156.700	156.700	Port Operations.  VTS in selected areas.

15	 --	  	156.75		Environmental (Receive only).  Used by Class C EPIRBs.

16	 156.800	156.800	International Distress, Safety and Calling.  Ships requiredto carry radio, USCG, and most coast stations maintain a		listening watch on this channel.

17	 156.850	156.850	State Control

18A	 156.900	156.900	Commercial

19A	 156.950	156.950	Commercial

20	 157.000	161.600	Port Operations (duplex)

20A	 157.000	157.000	Port Operations

21A	 157.050	157.050	U.S. Coast Guard only

22A	 157.100	157.100	Coast Guard Liaison and Maritime Safety Information Broadcasts. Broadcasts announced on channel 16.

23A	 157.150	157.150	U.S. Coast Guard only

24	 157.200	161.800	Public Correspondence (Marine Operator)

25	 157.250	161.850	Public Correspondence (Marine Operator)

26	 157.300	161.900	Public Correspondence (Marine Operator)

27	 157.350	161.950	Public Correspondence (Marine Operator)

28	 157.400	162.000	Public Correspondence (Marine Operator)

63A	 156.175	156.175	Port Operations and Commercial, VTS.  Available only in New Orleans / Lower Mississippi  area.

65A	 156.275	156.275	Port Operations

66A	 156.325	156.325	Port Operations

67	 156.375	  156.375		 Commercial.  Used for Bridge-to-bridge communications	in lower Mississippi River.  Intership only.

68	 156.425	156.425	Non-Commercial

69	 156.475	156.475	Non-Commercial

70	 156.525	156.525	Digital Selective Calling (voice communications not		allowed)

71	 156.575	156.575	Non-Commercial

72	 156.625	156.625	Non-Commercial (Intership only)

73	 156.675	156.675	Port Operations

74	 156.725	156.725	Port Operations

77	 156.875	156.875	Port Operations (Intership only)

78A	 156.925	156.925	Non-Commercial

79A	 156.975	156.975	Commercial.  Non-Commercial in Great Lakes only

80A	 157.025	157.025	Commercial.  Non-Commercial in Great Lakes only

81A	 157.075	157.075	U.S. Government only - Environmental protection operations.

82A	 157.125	157.125	U.S. Government only

83A	 157.175	157.175	U.S. Coast Guard only

84	 157.225	161.825	Public Correspondence (Marine Operator)

85	 157.275	161.875	Public Correspondence (Marine Operator)

86	 157.325	161.925	Public Correspondence (Marine Operator)

87	 157.375	161.975	Public Correspondence (Marine Operator)

88	 157.425	162.025	Public Correspondence only near Canadian border.

88A	 157.425	157.425	Commercial, Intership only.